## Slide 1: Introduction to CPACS
Marko Alder, Sebastian Wöhler
Institute of System Architectures in Aeronautics
DLR, Hamburg

## Slide 2: Agenda
  Introduction to CPACS
  APIs and libraries: TiXI and TiGL (Hands-on)
  Working with xsd schema

## Slide 3: Central Standard Data - Introduction
Operations
Aerodynamics
On board systems
Flight control
Management
Propulsion
Structure
Material
Mission performance
Disciplinary Experts

## Slide 4: Central Standard Data - Introduction
Common Parametric Aircraft Configuration Schema
Operations
Aerodynamics
On board systems
Flight control
Management
Propulsion
Structure
Material
Mission performance
Disciplinary Experts

## Slide 5: CPACS: Common Parametric Aircraft Configuration Schema
top level
2. level
3. level
4. level
Hierarchical Structure

## Slide 6: CPACS: Common Parametric Aircraft Configuration Schema
Common language for aircraft design
Exchange of specialist knowledge
Developed since 2005, based on XML / XSD
  Human readable
  Standardized
  Contains product and process information
  Open-source
top level
2. level
3. level
4. level
Hierarchical Structure

## Slide 7: CPACS: Common Parametric Aircraft Configuration Schema
Common language for aircraft design
Exchange of specialist knowledge
Developed since 2005, based on XML / XSD
  Human readable
  Reduced number of interfaces
  Standardized
  Product and process information
top level
2. level
3. level
4. level
Supporting libraries:
TIXI: fast & simple XML Interfacing
TIGL: Geometric Library (based on OpenCASCADE)
- query functions: tiglGetWingArea
- export to IGES/VTK
- geometry viewer
external interfaces for: C, C++, Python, Java, MATLAB and Fortran
Hierarchical Structure

## Slide 8: Using CPACS for parametric design
Optimization
Sensitivity
Iteration  Synthesis
Meta-Model
Datenbank
MDA System
Requirements
Parameter
Performance,
Properties
Engineering Service 2
Engineering Service n
Engineering Service 1
Design Optimization
Assessment
Multi-Disciplinary Modelling
Loads
Aerodynamics
Structure

## Slide 9: Using CPACS for parametric design
Optimization
Sensitivity
Iteration  Synthesis
Meta-Model
Datenbank
MDA System
Requirements
Parameter
Performance,
Properties
Engineering Service 2
Engineering Service n
Engineering Service 1
Design Optimization
Assessment
Multi-Fidelity Modelling
Euler
3D Panel
Lifting_Line

## Slide 10: Using CPACS for parametric design
Optimization
Sensitivity
Iteration  Synthesis
Meta-Model
Datenbank
MDA System
Requirements
Parameter
Performance,
Properties
Engineering Service 2
Engineering Service n
Engineering Service 1
Design Optimization
Assessment
Multi-Scale Modelling
Fleet
Aircraft
Component

## Slide 11: CPACS
CPACS is an aircraft „ontology“ defined in XML Schema Definition (XSD)
  It describes things and their relations using XSD syntax
CPACS is multi disciplinary and multi scale
  airlines & operations
  airports & runways
  aircraft performance, requirements, mission & loads
  components & subcomponents (high lift devices, fuel tanks, …)
  structural layout & details (ribs, spars, beams, stringers)
  decks, cabin geometry, aisles doors, floors, seats
CPACS contains ~1000 type definitions
CPACS is not a tool
CPACS contains no instances (but CPACS files do)
CPACS does not contain any functionality
  It can not compute, show or do anything
CPACS is the enabler for collaborative aircraft design
What CPACS is not:
What is CPACS?

## Slide 12: CPACS
fun
CPACS is the enabler for collaborative aircraft design
What is CPACS?

## Slide 13: CPACS eco-system documentation, support, development
GitHub
version management, Q&A forum
https://cpacs.de
Homepage
download, news, mailing list, online help, link to other parts of eco-system
https://github.com/DLR-SL/CPACS

## Slide 14: CPACS example file
https://github.com/DLR-SC/tigl/blob/master/tests/unittests/TestData/D150_v30.xml

## Slide 15: CPACS example file
<?xml version="1.0" encoding="utf-8"?>
<cpacs xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:noNamespaceSchemaLocation="cpacs_schema.xsd">
<header>
<name>D150 for CPACS 1.3</name>
…
</header>
<vehicles>
…
</vehicles>
</cpacs>
Informationen für Parser (XML-Version, Dekodierung)
Root-Element mit Namespace-Attributen

## Slide 16: TiXI
Download der Beispiele:
  https://docs.conda.io/en/latest/miniconda.html
  https://github.com/DLR-SL/CPACS_Seminar
Conda und Jupyter Notebook
  conda create -n python3_cpacs python=3.5 tigl3 tixi3 -c dlr-sc
  conda activate python3_cpacs
  conda install jupyter

## Slide 17: Python API: Basics
1. TiGL Workshop, September 11 / 12, Cologne
Martin Siggel
German Aerospace Center

## Slide 18: Outline
Motivation: Why a new low-level Python API?
Installation
Design and architecture
CPACS tree traversal with the tigl3.configuration module
Geometric components and named shapes
File exports with tigl3.exports
Practical session

## Slide 19: Motivation The old “high-level” API
Wraps the TiGL C API to Python
Used for many years by most of our users
Pros:
  Very easy to use
  Hides internal complexity of TiGL
Cons:
  Can do only what developers intended
  Very limited functionality
  No direct interaction with geometries
  Can be slow
We need a way, to access TiGL’s internals

## Slide 20: Motivation An example
Problem:
  Colleagues wanted to create wing cell geometries with different materials for FEM simulations of wind wheels
  Wing cells not modelled in TiGL
Solution:
    They used TiGL low-level python API with pythonOCC
    They created their own cell geometry code

## Slide 21: The Low-Level Python API
Why?
  We want to give you a flexible tool to be creative
  You are the experts: You should build your own models!
What do you get?
  Fast object-oriented access to all TiGL’s internals without compilation
  Full interoperability with OpenCASCADE (pythonOCC)
  Flexibility
  New geometry operations like Gordon surfaces
  Customizable file exports and imports
  Visualization with only a few code lines
  Create meshes using GMesh or SMesh
What do we get?
  We can focus on internals and algorithms
  Maybe more feedback or even contributions
Created with low-level API. ~50 lines of code

## Slide 22: Installation Conda
Conda: „Package, dependency and environment management for any language—Python, R, Ruby, Lua, Scala, Java, JavaScript, C/ C++, FORTRAN”
De-facto standard in scientific community
Differences to PIP:
  Packaging also non-Python packages like libraries, executables …
  Support for compiled binary packages
  Custom package repositories
Common to PIP:
  Virtual environments
  Large package repositories
  Update of packages
TiGL’s Conda repository: https://anaconda.org/DLR-SC/

## Slide 23: Installation Conda
>> conda install numpy matplotlib
>> source activate tigl_env
>> activate tigl_env
>> conda create -n tigl_env tigl3 python=3.5 –c dlr-sc
1. Install TiGL 3 into new virtual environment „tigl_env“ using python 3.5:
2. Switch into tigl_env environment:
3. There, install other packages or run python interpreter, e.g.:
(windows)
(mac/linux)

## Slide 24: Getting started
Have a look at the examples/python directory of TiGL!

## Slide 25: Design philosophy
Direct unaltered access to the internal C++ API
  Gives the same possibilities as if you were using the C++ interface
Full interoperability with OpenCASCADE
Provide additional wrapper functions to make use more pythonic
Small drawback: C++ API is not stable and sometimes changes (a bit)

## Slide 26: Architecture
OpenCASCADE bindings pythonOCC generated with SWIG software: http://www.swig.org/
TiGL low-level API also generated with SWIG from TiGL and pythonOCC
Objects between pythonOCC and TiGL can be exchanged
Input files for Swig can be found in: <TiGL-Source>/bindings/python_internal
SWIG can also generate bindings for other languages!
Small drawback: Bindings must be compiled for specific platform and python version!
OpenCASCADE CAD Kernel
TiGL
pythonOCC
TiXI
TiGL low-level Python API
TiGL hi-level Python API
via Swig
via ctypes
via Swig
native

## Slide 27: Internal Structure
Low-Level API consists of the following modules:
Module | Description
tigl3.configuration | Access to the whole cpacs tree including wings, fuselages …
tigl3.geometry | Functions related to geometry operations, e.g. curve interpolation
tigl3.curve_factories | Functions to create curves based on tigl3.geometry
tigl3.surface_factories | Functions to create surfaces based on tigl3.geometry
tigl3.occ_helpers | Pythonic wrappers to OpenCASCADE functions
tigl3.exports | File export classes
tigl3.imports | File import classes
tigl3.boolean_ops | Classes to perform Boolean operations
tigl3.tmath | A few math functions
tigl3.core | Core functionality, like error handling

## Slide 28: The tigl3.configuration module CPACS tree traversal
from tigl3 import tigl3wrapper
from tigl3.configuration import CCPACSConfigurationManager_get_instance
tigl_handle = tigl3wrapper.Tigl3()
tigl_handle.open(tixi_handle, "")
mgr = CCPACSConfigurationManager_get_instance()
aircraft_config = mgr.get_configuration(tigl_handle._handle.value)
TiGL handles several aircraft configurations at a time. To get a specific one, use the configuration manager class:
  Load the „old“ high-level python API
  Retrieve the global CCPACSConfigurationManager object
  Access a specific aircraft config, given by it‘s TiGL handle (integer value)
aircraft_config is instance of class CCPACSConfiguration. Gives direct access to fuselages, wings, systems …
1
2
0
1
0
2

## Slide 29: The tigl3.configuration module CPACS tree traversal
Use help to look for the available methods and members of each CPACS node
help(aircraft_config)
Examples:
  wing = aircraft_config.get_wing(1)
  wing = aircraft_config.get_wing("wing_uid")
  wing.get_uid()
  segment = wing.get_segment(2)
  segment = wing.get_segment("segment_uid")
  aircraft_config.get_fuselage(1)
  aircraft_config.get_uid()
Access wing spar properties:
  aircraft_config.get_wing(1).get_component_segment(1).get_structure().get_spar_segment(1) .get_spar_cross_section().get_rotation()
This way, accessing a specific object can be lengthy!

## Slide 30: The tigl3.configuration module UID Manager
Most objects that have a CPACS uid are registered at the UID manager when reading the CPACS file
The UID Manager is a member of the CCPACSConfiguration object
The UID Manager enables direct access to those objects:
    uid_mgr = aircraft_config.get_uidmanager() wing = uid_mgr.get_geometric_component("WingUID")
    spars = uid_mgr.get_geometric_component("SparSegmentsUID")
    …
Caveat: From Python only geometric components can be queried at the moment

## Slide 31: The tigl3.configuration module Geometric components
Cpacs nodes that have a geometry are a geometric component and derived from class ITiglGeometricComponent
To look, which geometric components currently are supported:
  Open TiGL Viewer
  Menu → Draw → Aircraft → Draw any component
These are today:
  Wings, Wing Segments, Fuselages, Fuselage Segments, Component Segments, Wing Cells, Wing Spars, Wing Ribs, Wing Chord Face, Wing Upper/Lower Side, External Components, Systems, Rotors, Rotor Blades, Fuselage Cross Beams, Fuselage Cross Beam Struts, Long Floors, Pressure Bulkheads, Doors
Access the geometry of geometric componenent with get_loft() method:
    wing.get_loft()

## Slide 32: Named Shapes Shapes with metadata
component.get_loft() returns an instance of tigl3.geometry.CNamedShape
Contains additional metadata next to the raw shape
Is used by the TiGL exports to write also identifiers and names
Allows to track the history of shape creation and modification, in particular after Boolean operations
Contains a graph of the shape creation history

## Slide 33: Named Shapes Shapes with metadata
Methods of tigl3.geometry.CNamedShape object are:
  .shape(): The actual shape as used by OpenCASCADE (OCC.TopoDS.TopoDS_Shape)
  .name(): The name of the shape (string)
  .short_name(): A short name of the shape (used for IGES identifiers)
  .get_face_traits(i): properties of the i-th face, including:
    .name(): Name of the face
    .set_name(): Set the name of the face
    .origin(): Shape from which the face was originally created from (CNamedShape)

## Slide 34: Named Shapes Creation and modification
Build from an OpenCASCADE shape, e.g.
    from tigl3.geometry import CNamedShape
    box = BRepPrimAPI_MakeBox(0.5, 0.5, 0.5).Shape() # Build a box with OpenCASCADE
    box_ns = CNamedShape(box, "MyBoxObj")
Get number of faces of the box
    print(box_ns.get_face_count()) # Should be 6
Print current name of the 4-th face
print(box_ns.get_face_traits(4).name())
Modify the name of the 4-th face
    box_ns.get_face_traits(4).set_name("bottom")

## Slide 35: The tigl3.export module
File exports are interfaces to simulation software or CAD programs
The tigl3.export module includes exports for the following file formats
Format | Description
Step (ISO 10303) | Current industry standard for CAD products.
IGES | Predecessor to Step. Standard file exchange format for CAD surfaces.
BRep | Native OpenCASCADE format to store shapes.
VTP (VTK Polydata Mesh) | Triangulated surface mesh for Paraview / VTK. Can include metadata.
STL | Simple surface mesh format. Used for 3D printers.
Collada | Standard format for 3D rendering software like Blender.

## Slide 36: The tigl3.export module CTiglCadExporter Interface
All exporters have a common interface CTiglCADExporter
The most important methods are
Method | Description
add_shape(named_shape, options) | Adds a (named) shape to the file. Options are exporter specific, e.g. IGES level, triangulation accuracy …
add_configuration(aircraft_config, options) | Adds the whole aircraft to the exporter
add_fused_configuration(aircraft_config, options) | Adds the fused aircraft to the exporter by trimming all surfaces first.
write(filename) | Writes the geometries to the specified file.
supported_file_type() | Returns semicolon separated list of supported file extensions, like “igs;iges”

## Slide 37: The tigl3.export module Example: Basic IGES Export
Write left and right wing + fuselage to test.iges:
    import tigl3.exports exporter = tigl3.exports.create_exporter("igs") exporter.add_shape(wing.get_loft())
    exporter.add_shape(wing.get_mirrored_loft())
    exporter.add_shape(fuselage.get_loft()) exporter.write("test.igs")

## Slide 38: The tigl3.export module Example: IGES Export with layers
The IGES file format supports layers that are used e.g. by mesh generators
Write fuselage and wing to separate layers 1111 and 2222:
    import tigl3.exports exporter = tigl3.exports.create_exporter("igs")
    exporter.add_shape(fuselage.get_loft(), tigl3.exports.IgesShapeOptions(1111)) exporter.add_shape(wing.get_loft(), tigl3.exports.IgesShapeOptions(2222)) exporter.write("test_layers.igs")
S0000001 ,,31HOpen CASCADE IGES processor 6.8,13HFilename.iges, G0000001 16HOpen CASCADE 6.8,31HOpen CASCADE IGES processor 6.8,32,308,15,308,15,G0000002 ,1.,2,2HMM,1,0.01,15H20180910.100150,0.000195405,2000.322906,4HTiGL, G0000003 33HGerman Aerospace Center (DLR), SC,11,0,15H20180910.100150,; G0000004 514 1 0 0 1111 0 0 000010000D0000001 514 0 0 1 1 F1 D0000002 510 2 0 0 1111 0 0 000010000D0000003 510 0 0 1 1 F1 D0000004 .
.
514 90 0 0 2222 0 0 000010000D0000079 514 0 0 1 1 W1 D0000080 510 91 0 0 2222 0 0 000010000D0000081 510 0 0 1 1 Bottom D0000082 128 92 0 0 0 0 0 000010000D0000083

## Slide 39: The tigl3.export module Example: IGES Export of whole aircraft with custom settings
Now lets export the whole aircraft.
Lets tweak the default settings:
  By default, the IGES export includes the far field and produces does not include symmetries
  Lets change this
    import tigl3.exports
    # get the current IGES settings and modify them iges_config = tigl3.exports.get_export_config("igs") iges_config.set_include_farfield(False) iges_config.set_apply_symmetries(True)
    # create the exporter with the new settings exporter = tigl3.exports.create_exporter("igs", iges_config) exporter.add_configuration(config) exporter.write("test.igs")

## Slide 40: The tigl3.import_export_helper module Convenience layer
Wrap the exporters in simple to use functions
Currently only one function: export_shapes(shapes, filename, deflection=0.001)
  Automatically determines exporter according to file extension
  Can also use OCC.TopoDS.TopoDS_Shapes
  Example:
    from tigl3.import_export_helper import export_shapes
    export_shapes([a_named_shape, a_topods_shape], "mystepfile.stp")

## Slide 41: Practical Session
Now it‘s your turn
Goal: Get to know the new API. Look around. Play around.
Possible Tasks:
  Install tigl3 via conda if not yet done
  Open exercise 1 from course material inside a jupyter notebook
  Load an aircraft configuration with TiXI and TiGL
  Access the first wing
  Check, which methods the CCPACSWing class offers
  Print the wing UID
  Get the shape of the wing
  Display all face names of the wing
  Rename the trailing edge of the wing
  Create named shape with a box
  Export wing and box to an IGES file with separate layers
  Drop exported *.igs file into TiGL Viewer to check.
  Open IGES file in text editor. What is in there?

## Slide 42: Fundamentals of data modeling with xml

## Slide 43: Fundamentals of data modeling with xml
<?xml version="1.0" encoding="UTF-8"?>
<xsd:schema xmlns:xsd="http://www.w3.org/2001/XMLSchema"
targetNamespace="http://www.w3.org/example_schema_v1"
xmlns="http://www.w3.org/example_schema_v1"
elementFormDefault="qualified">
</xsd:schema>

## Slide 44: Fundamentals of data modeling with xml

## Slide 45: Fundamentals of data modeling with xml
<xsd:all>
<xsd:sequence>
minOccurs="0"
minOccurs="0"
maxOccurs="unbounded"

## Slide 46: Fundamentals of data modeling with xml
<xsd:all>
<xsd:sequence>
<xsd:choice>
minOccurs="0"
minOccurs="0"
maxOccurs="unbounded"

## Slide 47: Fundamentals of data modeling with xml