## Slide 1: CPACS Introduction

## Slide 2: Central Standard Data - Introduction
Operations
Aerodynamics
On board systems
Flight control
Management
Propulsion
Structure
Material
Mission performance
Disciplinary Experts

## Slide 3: Central Standard Data - Introduction
Common Parametric Aircraft Configuration Schema
Operations
Aerodynamics
On board systems
Flight control
Management
Propulsion
Structure
Material
Mission performance
Disciplinary Experts

## Slide 4: CPACS: Common Parametric Aircraft Configuration Schema
top level
2. level
3. level
4. level
Hierarchical Structure

## Slide 5: CPACS: Common Parametric Aircraft Configuration Schema
Common language for aircraft design
Exchange of specialist knowledge
Developed since 2005, based on XML / XSD
  Human readable
  Standardized
  Contains product and process information
  Open-source
top level
2. level
3. level
4. level
Hierarchical Structure

## Slide 6: CPACS: Common Parametric Aircraft Configuration Schema
Common language for aircraft design
Exchange of specialist knowledge
Developed since 2005, based on XML / XSD
  Human readable
  Standardized
  Contains product and process information
  Open-source
top level
2. level
3. level
4. level
Supporting libraries:
TIXI: fast & simple XML Interfacing
TIGL: Geometric Library (based on OpenCASCADE)
- query functions: tiglGetWingArea
- export to IGES/VTK
- geometry viewer
external interfaces for: C, C++, Python, Java, MATLAB and Fortran
Hierarchical Structure

## Slide 7
Tool integration framework
Supports data exchange via CPACS files
Aircraft data ontology
Schema: XSD
Data: XML
Aircraft design tool
Python
TiXI
TiGL: TiGL Geometry Library
Based on OpenCascade
(Additional) methods for geometric operations
Viewer
TiXI: TiXI XML Interface
Extends LibXML2 with individual functionalities

## Slide 8: CPACS: Common Parametric Aircraft Configuration Schema
top level
2. level
3. level
4. level
Hierarchical Structure
existing analysis module
input
output
input
input
select
selection
map

execute analysis
supporting libraries (optional)
file handling
geometry handling
provide output
output
output
output
updated
map

automate

## Slide 9: XSD and XML

## Slide 10: Using CPACS for parametric design
Optimization
Sensitivity
Iteration  Synthesis
Meta-Model
Datenbank
MDA System
Requirements
Parameter
Performance,
Properties
Engineering Service 2
Engineering Service n
Engineering Service 1
Design Optimization
Assessment
Multi-Disciplinary Modelling
Loads
Aerodynamics
Structure

## Slide 11: Using CPACS for parametric design
Optimization
Sensitivity
Iteration  Synthesis
Meta-Model
Datenbank
MDA System
Requirements
Parameter
Performance,
Properties
Engineering Service 2
Engineering Service n
Engineering Service 1
Design Optimization
Assessment
Multi-Fidelity Modelling
Euler
3D Panel
Lifting_Line

## Slide 12: Using CPACS for parametric design
Optimization
Sensitivity
Iteration  Synthesis
Meta-Model
Datenbank
MDA System
Requirements
Parameter
Performance,
Properties
Engineering Service 2
Engineering Service n
Engineering Service 1
Design Optimization
Assessment
Multi-Scale Modelling
Fleet
Aircraft
Component

## Slide 13: CPACS
CPACS is an aircraft „ontology“ defined in XML Schema Definition (XSD)
  It describes things and their relations using XS.D syntax
CPACS is multi disciplinary and multi scale
  airlines & operations
  airports & runways
  aircraft performance, requirements, mission & loads
  components & subcomponents (high lift devices, fuel tanks, …)
  structural layout & details (ribs, spars, beams, stringers)
  decks, cabin geometry, aisles doors, floors, seats
CPACS contains ~1000 type definitions
CPACS is not a tool
CPACS does not contain any functionality
  It can not compute, show or do anything
CPACS is the enabler for collaborative aircraft design
What CPACS is not:
What is CPACS?

## Slide 14: CPACS eco-system documentation, support, development
GitHub
version management, Q&A forum
https://cpacs.de
Homepage
download, news, newsletter, online help, link to other parts of eco-system
https://github.com/DLR-SL/CPACS

## Slide 15: Data modeling via XML

## Slide 16: XSD and XML

## Slide 17: XSD and XML
XML
XSD
<?xml version="1.0" encoding="UTF-8"?>
<aircraft xmlns="http://www.w3.org/aircraft_schema" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.w3.org/aircraft_schema aircraft_schema.xsd ">
<fuselages>
<fuselage uID="fuselageRandomID">
<diameter>5</diameter>
</fuselage>
</fuselages>
<wings>wings</wings>
</aircraft>

## Slide 18: XSD and XML
XSD
Elements
Types
Simple types
Complex types
Occurence
all
choice
sequence
Attributes

## Slide 19: XSD and XML
XSD

## Slide 20: XSD and XML
Element name
Type of the element
Parents
Children
Occurences
Description
Attributes

## Slide 21: Development process

## Slide 22: Development process

## Slide 23: Development process
Pre-Release anouncement
> 4 weeks

## Slide 24: Development process
https://github.com/DLR-SL/CPACS/tree/develop/development
https://github.com/DLR-SL/CPACS_Seminar